## Slide 1: IP Subnetting – Zero to Hero Subnetting with VLSM
CyberQuince

## Slide 2: Example 1
A company uses the 10.0.0.0 /8 address range. They want to create smaller subnets, and these are their requirements:
  Two subnets with 500 hosts each;
  One subnet with 220 hosts;
  Four subnets with 50 hosts each;
  Three subnets with 10 hosts each;
  Two point-to-point subnets.

## Slide 3: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses

## Slide 4: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 |  |  |  | 
500 |  |  |  | 
220 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 

## Slide 5: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 |  |  | 
500 |  |  |  | 
220 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 

## Slide 6: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 |  |  | 
500 |  |  |  | 
220 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000000 . 00000000

## Slide 7: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 |  |  | 
500 |  |  |  | 
220 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000000 . 00000000

## Slide 8: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 |  |  | 
500 |  |  |  | 
220 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000000 . 00000000
29 = 512

## Slide 9: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 |  | 
500 |  |  |  | 
220 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000000 . 00000000
29 = 512

## Slide 10: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 |  | 
500 |  |  |  | 
220 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000001 . 11111111

## Slide 11: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 |  | 
500 |  |  |  | 
220 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000001 . 11111111
1

## Slide 12: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 |  | 
500 |  |  |  | 
220 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000001 . 11111111
1
255

## Slide 13: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 
500 |  |  |  | 
220 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000001 . 11111111
1
255

## Slide 14: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1
500 |  |  |  | 
220 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000001 . 11111111
1
255

## Slide 15: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 –
500 |  |  |  | 
220 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000001 . 11111111
1
255

## Slide 16: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 |  |  |  | 
220 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000001 . 11111111
1
255

## Slide 17: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 |  |  | 
220 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000001 . 11111111

## Slide 18: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 |  |  | 
220 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000010 . 00000000

## Slide 19: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 |  | 
220 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000010 . 00000000

## Slide 20: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 |  | 
220 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000011 . 11111111

## Slide 21: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 |  | 
220 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000011 . 11111111
3

## Slide 22: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 |  | 
220 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000011 . 11111111
3
255

## Slide 23: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 
220 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000011 . 11111111
3
255

## Slide 24: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1
220 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000011 . 11111111
3
255

## Slide 25: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000011 . 11111111
3
255

## Slide 26: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000011 . 11111111

## Slide 27: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000011 . 11111111

## Slide 28: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000100 . 00000000

## Slide 29: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000100 . 00000000

## Slide 30: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000100 . 00000000

## Slide 31: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000100 . 11111111

## Slide 32: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000100 . 11111111

## Slide 33: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000100 . 11111111

## Slide 34: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000100 . 11111111

## Slide 35: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000100 . 11111111

## Slide 36: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000100 . 11111111

## Slide 37: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000101 . 11111111

## Slide 38: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000101 . 00000000

## Slide 39: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 |  |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000101 . 00000000

## Slide 40: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000101 . 00000000

## Slide 41: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 |  | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000101 . 00111111

## Slide 42: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000101 . 00111111

## Slide 43: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000101 . 00111111

## Slide 44: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 |  |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000101 . 00111111

## Slide 45: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000101 . 00111111

## Slide 46: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 |  |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000101 . 01000000

## Slide 47: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000101 . 01000000

## Slide 48: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000101 . 01111111

## Slide 49: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000101 . 01111111
63

## Slide 50: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 |  | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000101 . 01111111
127

## Slide 51: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000101 . 01111111
127

## Slide 52: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000101 . 01111111
127

## Slide 53: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 |  |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000101 . 01111111
127

## Slide 54: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000101 . 01111111
127

## Slide 55: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 |  |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000101 . 10000000

## Slide 56: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000101 . 10000000

## Slide 57: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000101 . 10111111

## Slide 58: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000101 . 10111111
63

## Slide 59: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000101 . 10111111
63
128

## Slide 60: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000101 . 10111111
63
128 +

## Slide 61: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000101 . 10111111
63 =
128 +

## Slide 62: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 |  | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000101 . 10111111
63 = 191
128 +

## Slide 63: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000101 . 10111111
63 = 191
128 +

## Slide 64: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000101 . 10111111
63 = 191
128 +

## Slide 65: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000101 . 10111111
63 = 191
128 +

## Slide 66: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000101 . 10111111
63 = 191
128 +

## Slide 67: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000101 . 10111111

## Slide 68: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 |  |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000101 . 11000000

## Slide 69: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000101 . 11000000

## Slide 70: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 |  | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000101 . 11111111

## Slide 71: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000101 . 11111111

## Slide 72: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000101 . 11111111

## Slide 73: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 |  |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000101 . 11111111

## Slide 74: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000101 . 11111111

## Slide 75: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000101 . 11111111

## Slide 76: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000101 . 00000000

## Slide 77: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000101 . 00000000
5

## Slide 78: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000110 . 00000000
6

## Slide 79: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 |  |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000110 . 00000000
6

## Slide 80: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000110 . 00000000
6

## Slide 81: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000110 . 00000000
6
/28 =

## Slide 82: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000110 . 00000000
6
/28 = 11111111.11111111.11111111.11110000

## Slide 83: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000110 . 00000000
6
/28 = 11111111.11111111.11111111.11110000
255

## Slide 84: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000110 . 00000000
6
/28 = 11111111.11111111.11111111.11110000
255 255

## Slide 85: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000110 . 00000000
6
/28 = 11111111.11111111.11111111.11110000
255 255 255

## Slide 86: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000110 . 00000000
6
/28 = 11111111.11111111.11111111.11110000
255 255 255 240

## Slide 87: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000110 . 00000000
6

## Slide 88: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000110 . 00001111
6

## Slide 89: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 |  | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000110 . 00001111
6
15

## Slide 90: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 | 10.0.6.15 | 
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000110 . 00001111
6
15

## Slide 91: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 | 10.0.6.15 | 10.0.6.1 – 10.0.6.14
10 |  |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000110 . 00001111
6
15

## Slide 92: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 | 10.0.6.15 | 10.0.6.1 – 10.0.6.14
10 | 10.0.6.16 |  |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000110 . 00001111
6
15

## Slide 93: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 | 10.0.6.15 | 10.0.6.1 – 10.0.6.14
10 | 10.0.6.16 | /28 |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000110 . 00001111
6
15

## Slide 94: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 | 10.0.6.15 | 10.0.6.1 – 10.0.6.14
10 | 10.0.6.16 | /28 |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000110 . 00001111
6

## Slide 95: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 | 10.0.6.15 | 10.0.6.1 – 10.0.6.14
10 | 10.0.6.16 | /28 |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000110 . 00011111
6

## Slide 96: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 | 10.0.6.15 | 10.0.6.1 – 10.0.6.14
10 | 10.0.6.16 | /28 |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000110 . 00010000
6

## Slide 97: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 | 10.0.6.15 | 10.0.6.1 – 10.0.6.14
10 | 10.0.6.16 | /28 |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000110 . 00010000
6
16

## Slide 98: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 | 10.0.6.15 | 10.0.6.1 – 10.0.6.14
10 | 10.0.6.16 | /28 |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000110 . 00011111
6

## Slide 99: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 | 10.0.6.15 | 10.0.6.1 – 10.0.6.14
10 | 10.0.6.16 | /28 |  | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000110 . 00011111
6
31

## Slide 100: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 | 10.0.6.15 | 10.0.6.1 – 10.0.6.14
10 | 10.0.6.16 | /28 | 10.0.6.31 | 
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000110 . 00011111
6
31

## Slide 101: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 | 10.0.6.15 | 10.0.6.1 – 10.0.6.14
10 | 10.0.6.16 | /28 | 10.0.6.31 | 10.0.6.17 – 10.0.6.30
10 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000110 . 00011111
6
31

## Slide 102: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 | 10.0.6.15 | 10.0.6.1 – 10.0.6.14
10 | 10.0.6.16 | /28 | 10.0.6.31 | 10.0.6.17 – 10.0.6.30
10 | 10.0.6.32 |  |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000110 . 00011111
6
31

## Slide 103: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 | 10.0.6.15 | 10.0.6.1 – 10.0.6.14
10 | 10.0.6.16 | /28 | 10.0.6.31 | 10.0.6.17 – 10.0.6.30
10 | 10.0.6.32 | /28 |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000110 . 00011111
6
31

## Slide 104: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 | 10.0.6.15 | 10.0.6.1 – 10.0.6.14
10 | 10.0.6.16 | /28 | 10.0.6.31 | 10.0.6.17 – 10.0.6.30
10 | 10.0.6.32 | /28 |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000110 . 00100000
6
32

## Slide 105: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 | 10.0.6.15 | 10.0.6.1 – 10.0.6.14
10 | 10.0.6.16 | /28 | 10.0.6.31 | 10.0.6.17 – 10.0.6.30
10 | 10.0.6.32 | /28 |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000110 . 00101111
6
32

## Slide 106: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 | 10.0.6.15 | 10.0.6.1 – 10.0.6.14
10 | 10.0.6.16 | /28 | 10.0.6.31 | 10.0.6.17 – 10.0.6.30
10 | 10.0.6.32 | /28 |  | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000110 . 00101111
6
47

## Slide 107: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 | 10.0.6.15 | 10.0.6.1 – 10.0.6.14
10 | 10.0.6.16 | /28 | 10.0.6.31 | 10.0.6.17 – 10.0.6.30
10 | 10.0.6.32 | /28 | 10.0.6.47 | 
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000110 . 00101111
6
47

## Slide 108: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 | 10.0.6.15 | 10.0.6.1 – 10.0.6.14
10 | 10.0.6.16 | /28 | 10.0.6.31 | 10.0.6.17 – 10.0.6.30
10 | 10.0.6.32 | /28 | 10.0.6.47 | 10.0.6.33 – 10.0.6.46
4 |  |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000110 . 00101111
6
47

## Slide 109: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 | 10.0.6.15 | 10.0.6.1 – 10.0.6.14
10 | 10.0.6.16 | /28 | 10.0.6.31 | 10.0.6.17 – 10.0.6.30
10 | 10.0.6.32 | /28 | 10.0.6.47 | 10.0.6.33 – 10.0.6.46
4 | 10.0.6.48 |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000110 . 00101111
6
47

## Slide 110: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 | 10.0.6.15 | 10.0.6.1 – 10.0.6.14
10 | 10.0.6.16 | /28 | 10.0.6.31 | 10.0.6.17 – 10.0.6.30
10 | 10.0.6.32 | /28 | 10.0.6.47 | 10.0.6.33 – 10.0.6.46
4 | 10.0.6.48 |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000110 . 00110000
6
48

## Slide 111: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 | 10.0.6.15 | 10.0.6.1 – 10.0.6.14
10 | 10.0.6.16 | /28 | 10.0.6.31 | 10.0.6.17 – 10.0.6.30
10 | 10.0.6.32 | /28 | 10.0.6.47 | 10.0.6.33 – 10.0.6.46
4 | 10.0.6.48 |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000110 . 00110000
6
48

## Slide 112: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 | 10.0.6.15 | 10.0.6.1 – 10.0.6.14
10 | 10.0.6.16 | /28 | 10.0.6.31 | 10.0.6.17 – 10.0.6.30
10 | 10.0.6.32 | /28 | 10.0.6.47 | 10.0.6.33 – 10.0.6.46
4 | 10.0.6.48 |  |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000110 . 00110000
6
48

## Slide 113: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 | 10.0.6.15 | 10.0.6.1 – 10.0.6.14
10 | 10.0.6.16 | /28 | 10.0.6.31 | 10.0.6.17 – 10.0.6.30
10 | 10.0.6.32 | /28 | 10.0.6.47 | 10.0.6.33 – 10.0.6.46
4 | 10.0.6.48 | /30 |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000110 . 00110000
6
48

## Slide 114: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 | 10.0.6.15 | 10.0.6.1 – 10.0.6.14
10 | 10.0.6.16 | /28 | 10.0.6.31 | 10.0.6.17 – 10.0.6.30
10 | 10.0.6.32 | /28 | 10.0.6.47 | 10.0.6.33 – 10.0.6.46
4 | 10.0.6.48 | /30 |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000110 . 00110011
6
48

## Slide 115: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 | 10.0.6.15 | 10.0.6.1 – 10.0.6.14
10 | 10.0.6.16 | /28 | 10.0.6.31 | 10.0.6.17 – 10.0.6.30
10 | 10.0.6.32 | /28 | 10.0.6.47 | 10.0.6.33 – 10.0.6.46
4 | 10.0.6.48 | /30 |  | 
4 |  |  |  | 
00001010 . 00000000 . 00000110 . 00110011
6
51

## Slide 116: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 | 10.0.6.15 | 10.0.6.1 – 10.0.6.14
10 | 10.0.6.16 | /28 | 10.0.6.31 | 10.0.6.17 – 10.0.6.30
10 | 10.0.6.32 | /28 | 10.0.6.47 | 10.0.6.33 – 10.0.6.46
4 | 10.0.6.48 | /30 | 10.0.6.51 | 
4 |  |  |  | 
00001010 . 00000000 . 00000110 . 00110011
6
51

## Slide 117: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 | 10.0.6.15 | 10.0.6.1 – 10.0.6.14
10 | 10.0.6.16 | /28 | 10.0.6.31 | 10.0.6.17 – 10.0.6.30
10 | 10.0.6.32 | /28 | 10.0.6.47 | 10.0.6.33 – 10.0.6.46
4 | 10.0.6.48 | /30 | 10.0.6.51 | 10.0.6.49 – 10.0.6.50
4 |  |  |  | 
00001010 . 00000000 . 00000110 . 00110011
6
51

## Slide 118: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 | 10.0.6.15 | 10.0.6.1 – 10.0.6.14
10 | 10.0.6.16 | /28 | 10.0.6.31 | 10.0.6.17 – 10.0.6.30
10 | 10.0.6.32 | /28 | 10.0.6.47 | 10.0.6.33 – 10.0.6.46
4 | 10.0.6.48 | /30 | 10.0.6.51 | 10.0.6.49 – 10.0.6.50
4 | 10.0.6.52 |  |  | 
00001010 . 00000000 . 00000110 . 00110011
6
51

## Slide 119: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 | 10.0.6.15 | 10.0.6.1 – 10.0.6.14
10 | 10.0.6.16 | /28 | 10.0.6.31 | 10.0.6.17 – 10.0.6.30
10 | 10.0.6.32 | /28 | 10.0.6.47 | 10.0.6.33 – 10.0.6.46
4 | 10.0.6.48 | /30 | 10.0.6.51 | 10.0.6.49 – 10.0.6.50
4 | 10.0.6.52 |  |  | 
00001010 . 00000000 . 00000110 . 00110100
6
52

## Slide 120: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 | 10.0.6.15 | 10.0.6.1 – 10.0.6.14
10 | 10.0.6.16 | /28 | 10.0.6.31 | 10.0.6.17 – 10.0.6.30
10 | 10.0.6.32 | /28 | 10.0.6.47 | 10.0.6.33 – 10.0.6.46
4 | 10.0.6.48 | /30 | 10.0.6.51 | 10.0.6.49 – 10.0.6.50
4 | 10.0.6.52 | /30 |  | 
00001010 . 00000000 . 00000110 . 00110100
6
52

## Slide 121: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 | 10.0.6.15 | 10.0.6.1 – 10.0.6.14
10 | 10.0.6.16 | /28 | 10.0.6.31 | 10.0.6.17 – 10.0.6.30
10 | 10.0.6.32 | /28 | 10.0.6.47 | 10.0.6.33 – 10.0.6.46
4 | 10.0.6.48 | /30 | 10.0.6.51 | 10.0.6.49 – 10.0.6.50
4 | 10.0.6.52 | /30 |  | 
00001010 . 00000000 . 00000110 . 00110111
6
55

## Slide 122: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 | 10.0.6.15 | 10.0.6.1 – 10.0.6.14
10 | 10.0.6.16 | /28 | 10.0.6.31 | 10.0.6.17 – 10.0.6.30
10 | 10.0.6.32 | /28 | 10.0.6.47 | 10.0.6.33 – 10.0.6.46
4 | 10.0.6.48 | /30 | 10.0.6.51 | 10.0.6.49 – 10.0.6.50
4 | 10.0.6.52 | /30 | 10.0.6.55 | 
00001010 . 00000000 . 00000110 . 00110111
6
55

## Slide 123: Example 1
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
500 | 10.0.0.0 | /23 | 10.0.1.255 | 10.0.0.1 – 10.0.1.254
500 | 10.0.2.0 | /23 | 10.0.3.255 | 10.0.2.1 – 10.0.3.254
220 | 10.0.4.0 | /24 | 10.0.4.255 | 10.0.4.1 – 10.0.4.254
50 | 10.0.5.0 | /26 | 10.0.5.63 | 10.0.5.1 – 10.0.5.62
50 | 10.0.5.64 | /26 | 10.0.5.127 | 10.0.5.65 – 10.0.5.126
50 | 10.0.5.128 | /26 | 10.0.5.191 | 10.0.5.129 – 10.0.5.190
50 | 10.0.5.192 | /26 | 10.0.5.255 | 10.0.5.193 – 10.0.5.254
10 | 10.0.6.0 | /28 | 10.0.6.15 | 10.0.6.1 – 10.0.6.14
10 | 10.0.6.16 | /28 | 10.0.6.31 | 10.0.6.17 – 10.0.6.30
10 | 10.0.6.32 | /28 | 10.0.6.47 | 10.0.6.33 – 10.0.6.46
4 | 10.0.6.48 | /30 | 10.0.6.51 | 10.0.6.49 – 10.0.6.50
4 | 10.0.6.52 | /30 | 10.0.6.55 | 10.0.6.53 – 10.0.6.54
00001010 . 00000000 . 00000110 . 00110111
6
55

## Slide 124: IP Subnetting – Zero to Hero Subnetting with VLSM
CyberQuince

## Slide 125: Example 1
Text