## Slide 1: IP Subnetting – Zero to Hero Subnetting with VLSM
CyberQuince

## Slide 2: Example 2
A company uses a public range 176.33.202.0 /23. They want to create smaller subnets, and these are their requirements:
  Two point-to-point subnets;
  One subnet with 100 hosts;
  Three subnets with 4 hosts each;
  Two subnets with 13 hosts each;

## Slide 3: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses

## Slide 4: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 |  |  |  | 
15 |  |  |  | 
15 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 

## Slide 5: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 |  |  | 
15 |  |  |  | 
15 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 

## Slide 6: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 |  |  | 
15 |  |  |  | 
15 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
10110000 . 00100001 . 1100101 0 . 00000000

## Slide 7: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 |  |  | 
15 |  |  |  | 
15 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
10110000 . 00100001 . 1100101 0 . 00000000

## Slide 8: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 |  |  | 
15 |  |  |  | 
15 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
10110000 . 00100001 . 1100101 0 . 00000000
27 = 128

## Slide 9: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 | /25 |  | 
15 |  |  |  | 
15 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
10110000 . 00100001 . 1100101 0 . 00000000
27 = 128

## Slide 10: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 | /25 |  | 
15 |  |  |  | 
15 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
10110000 . 00100001 . 1100101 0 . 01111111

## Slide 11: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 | /25 |  | 
15 |  |  |  | 
15 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
10110000 . 00100001 . 1100101 0 . 01111111

## Slide 12: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 | /25 |  | 
15 |  |  |  | 
15 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
10110000 . 00100001 . 1100101 0 . 01111111
127

## Slide 13: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 | /25 | 176.33.202.127 | 
15 |  |  |  | 
15 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
10110000 . 00100001 . 1100101 0 . 01111111
127

## Slide 14: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 | /25 | 176.33.202.127 | 176.33.202.1 – 176.33.202.126
15 |  |  |  | 
15 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
10110000 . 00100001 . 1100101 0 . 01111111
127

## Slide 15: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 | /25 | 176.33.202.127 | 176.33.202.1 – 176.33.202.126
15 |  |  |  | 
15 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
10110000 . 00100001 . 1100101 0 . 01111111

## Slide 16: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 | /25 | 176.33.202.127 | 176.33.202.1 – 176.33.202.126
15 | 176.33.202.128 |  |  | 
15 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
10110000 . 00100001 . 1100101 0 . 01111111

## Slide 17: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 | /25 | 176.33.202.127 | 176.33.202.1 – 176.33.202.126
15 | 176.33.202.128 |  |  | 
15 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
10110000 . 00100001 . 1100101 0 . 10000000

## Slide 18: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 | /25 | 176.33.202.127 | 176.33.202.1 – 176.33.202.126
15 | 176.33.202.128 |  |  | 
15 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
10110000 . 00100001 . 1100101 0 . 10000000

## Slide 19: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 | /25 | 176.33.202.127 | 176.33.202.1 – 176.33.202.126
15 | 176.33.202.128 | /28 |  | 
15 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
10110000 . 00100001 . 1100101 0 . 10000000

## Slide 20: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 | /25 | 176.33.202.127 | 176.33.202.1 – 176.33.202.126
15 | 176.33.202.128 | /28 |  | 
15 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
10110000 . 00100001 . 1100101 0 . 10001111

## Slide 21: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 | /25 | 176.33.202.127 | 176.33.202.1 – 176.33.202.126
15 | 176.33.202.128 | /28 |  | 
15 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
10110000 . 00100001 . 1100101 0 . 10001111
143

## Slide 22: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 | /25 | 176.33.202.127 | 176.33.202.1 – 176.33.202.126
15 | 176.33.202.128 | /28 | 176.33.202.143 | 176.33.202.129 – 176.33.202.142
15 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
10110000 . 00100001 . 1100101 0 . 10001111
143

## Slide 23: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 | /25 | 176.33.202.127 | 176.33.202.1 – 176.33.202.126
15 | 176.33.202.128 | /28 | 176.33.202.143 | 176.33.202.129 – 176.33.202.142
15 | 176.33.202.144 | /28 |  | 
6 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
10110000 . 00100001 . 1100101 0 . 10001111
143

## Slide 24: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 | /25 | 176.33.202.127 | 176.33.202.1 – 176.33.202.126
15 | 176.33.202.128 | /28 | 176.33.202.143 | 176.33.202.129 – 176.33.202.142
15 | 176.33.202.144 | /28 |  | 
6 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
10110000 . 00100001 . 1100101 0 . 10010000
144

## Slide 25: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 | /25 | 176.33.202.127 | 176.33.202.1 – 176.33.202.126
15 | 176.33.202.128 | /28 | 176.33.202.143 | 176.33.202.129 – 176.33.202.142
15 | 176.33.202.144 | /28 |  | 
6 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
10110000 . 00100001 . 1100101 0 . 10011111
159

## Slide 26: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 | /25 | 176.33.202.127 | 176.33.202.1 – 176.33.202.126
15 | 176.33.202.128 | /28 | 176.33.202.143 | 176.33.202.129 – 176.33.202.142
15 | 176.33.202.144 | /28 | 176.33.202.159 | 
6 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
10110000 . 00100001 . 1100101 0 . 10011111
159

## Slide 27: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 | /25 | 176.33.202.127 | 176.33.202.1 – 176.33.202.126
15 | 176.33.202.128 | /28 | 176.33.202.143 | 176.33.202.129 – 176.33.202.142
15 | 176.33.202.144 | /28 | 176.33.202.159 | 176.33.202.145 – 176.33.202.158
6 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
10110000 . 00100001 . 1100101 0 . 10011111
159

## Slide 28: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 | /25 | 176.33.202.127 | 176.33.202.1 – 176.33.202.126
15 | 176.33.202.128 | /28 | 176.33.202.143 | 176.33.202.129 – 176.33.202.142
15 | 176.33.202.144 | /28 | 176.33.202.159 | 176.33.202.145 – 176.33.202.158
6 |  |  |  | 
6 |  |  |  | 
6 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
10110000 . 00100001 . 1100101 0 . 10011111

## Slide 29: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 | /25 | 176.33.202.127 | 176.33.202.1 – 176.33.202.126
15 | 176.33.202.128 | /28 | 176.33.202.143 | 176.33.202.129 – 176.33.202.142
15 | 176.33.202.144 | /28 | 176.33.202.159 | 176.33.202.145 – 176.33.202.158
6 | 176.33.202.160 |  |  | 
6 |  |  |  | 
6 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
10110000 . 00100001 . 1100101 0 . 10011111

## Slide 30: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 | /25 | 176.33.202.127 | 176.33.202.1 – 176.33.202.126
15 | 176.33.202.128 | /28 | 176.33.202.143 | 176.33.202.129 – 176.33.202.142
15 | 176.33.202.144 | /28 | 176.33.202.159 | 176.33.202.145 – 176.33.202.158
6 | 176.33.202.160 | /29 |  | 
6 |  |  |  | 
6 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
10110000 . 00100001 . 1100101 0 . 10100000

## Slide 31: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 | /25 | 176.33.202.127 | 176.33.202.1 – 176.33.202.126
15 | 176.33.202.128 | /28 | 176.33.202.143 | 176.33.202.129 – 176.33.202.142
15 | 176.33.202.144 | /28 | 176.33.202.159 | 176.33.202.145 – 176.33.202.158
6 | 176.33.202.160 | /29 | 176.33.202.167 | 
6 |  |  |  | 
6 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
10110000 . 00100001 . 1100101 0 . 10100111
167

## Slide 32: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 | /25 | 176.33.202.127 | 176.33.202.1 – 176.33.202.126
15 | 176.33.202.128 | /28 | 176.33.202.143 | 176.33.202.129 – 176.33.202.142
15 | 176.33.202.144 | /28 | 176.33.202.159 | 176.33.202.145 – 176.33.202.158
6 | 176.33.202.160 | /29 | 176.33.202.167 | 176.33.202.161 – 176.33.202.166
6 |  |  |  | 
6 |  |  |  | 
4 |  |  |  | 
4 |  |  |  | 
10110000 . 00100001 . 1100101 0 . 10100111
167

## Slide 33: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 | /25 | 176.33.202.127 | 176.33.202.1 – 176.33.202.126
15 | 176.33.202.128 | /28 | 176.33.202.143 | 176.33.202.129 – 176.33.202.142
15 | 176.33.202.144 | /28 | 176.33.202.159 | 176.33.202.145 – 176.33.202.158
6 | 176.33.202.160 | /29 | 176.33.202.167 | 176.33.202.161 – 176.33.202.166
6 |  | /29 |  | 
6 |  | /29 |  | 
4 |  |  |  | 
4 |  |  |  | 
10110000 . 00100001 . 1100101 0 . 10100111
167

## Slide 34: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 | /25 | 176.33.202.127 | 176.33.202.1 – 176.33.202.126
15 | 176.33.202.128 | /28 | 176.33.202.143 | 176.33.202.129 – 176.33.202.142
15 | 176.33.202.144 | /28 | 176.33.202.159 | 176.33.202.145 – 176.33.202.158
6 | 176.33.202.160 | /29 | 176.33.202.167 | 176.33.202.161 – 176.33.202.166
6 | 176.33.202.168 | /29 |  | 
6 |  | /29 |  | 
4 |  |  |  | 
4 |  |  |  | 
10110000 . 00100001 . 1100101 0 . 10100111
167

## Slide 35: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 | /25 | 176.33.202.127 | 176.33.202.1 – 176.33.202.126
15 | 176.33.202.128 | /28 | 176.33.202.143 | 176.33.202.129 – 176.33.202.142
15 | 176.33.202.144 | /28 | 176.33.202.159 | 176.33.202.145 – 176.33.202.158
6 | 176.33.202.160 | /29 | 176.33.202.167 | 176.33.202.161 – 176.33.202.166
6 | 176.33.202.168 | /29 |  | 
6 | 176.33.202.176 | /29 |  | 
4 |  |  |  | 
4 |  |  |  | 
10110000 . 00100001 . 1100101 0 . 10100111
167

## Slide 36: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 | /25 | 176.33.202.127 | 176.33.202.1 – 176.33.202.126
15 | 176.33.202.128 | /28 | 176.33.202.143 | 176.33.202.129 – 176.33.202.142
15 | 176.33.202.144 | /28 | 176.33.202.159 | 176.33.202.145 – 176.33.202.158
6 | 176.33.202.160 | /29 | 176.33.202.167 | 176.33.202.161 – 176.33.202.166
6 | 176.33.202.168 | /29 |  | 
6 | 176.33.202.176 | /29 |  | 
4 | 176.33.202.184 |  |  | 
4 |  |  |  | 
10110000 . 00100001 . 1100101 0 . 10100111
167

## Slide 37: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 | /25 | 176.33.202.127 | 176.33.202.1 – 176.33.202.126
15 | 176.33.202.128 | /28 | 176.33.202.143 | 176.33.202.129 – 176.33.202.142
15 | 176.33.202.144 | /28 | 176.33.202.159 | 176.33.202.145 – 176.33.202.158
6 | 176.33.202.160 | /29 | 176.33.202.167 | 176.33.202.161 – 176.33.202.166
6 | 176.33.202.168 | /29 | 176.33.202.175 | 
6 | 176.33.202.176 | /29 |  | 
4 | 176.33.202.184 |  |  | 
4 |  |  |  | 
10110000 . 00100001 . 1100101 0 . 10100111
167

## Slide 38: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 | /25 | 176.33.202.127 | 176.33.202.1 – 176.33.202.126
15 | 176.33.202.128 | /28 | 176.33.202.143 | 176.33.202.129 – 176.33.202.142
15 | 176.33.202.144 | /28 | 176.33.202.159 | 176.33.202.145 – 176.33.202.158
6 | 176.33.202.160 | /29 | 176.33.202.167 | 176.33.202.161 – 176.33.202.166
6 | 176.33.202.168 | /29 | 176.33.202.175 | 
6 | 176.33.202.176 | /29 | 176.33.202.183 | 
4 | 176.33.202.184 |  |  | 
4 |  |  |  | 
10110000 . 00100001 . 1100101 0 . 10100111
167

## Slide 39: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 | /25 | 176.33.202.127 | 176.33.202.1 – 176.33.202.126
15 | 176.33.202.128 | /28 | 176.33.202.143 | 176.33.202.129 – 176.33.202.142
15 | 176.33.202.144 | /28 | 176.33.202.159 | 176.33.202.145 – 176.33.202.158
6 | 176.33.202.160 | /29 | 176.33.202.167 | 176.33.202.161 – 176.33.202.166
6 | 176.33.202.168 | /29 | 176.33.202.175 | 176.33.202.169 – 176.33.202.174
6 | 176.33.202.176 | /29 | 176.33.202.183 | 176.33.202.177 – 176.33.202.182
4 | 176.33.202.184 |  |  | 
4 |  |  |  | 
10110000 . 00100001 . 1100101 0 . 10100111
167

## Slide 40: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 | /25 | 176.33.202.127 | 176.33.202.1 – 176.33.202.126
15 | 176.33.202.128 | /28 | 176.33.202.143 | 176.33.202.129 – 176.33.202.142
15 | 176.33.202.144 | /28 | 176.33.202.159 | 176.33.202.145 – 176.33.202.158
6 | 176.33.202.160 | /29 | 176.33.202.167 | 176.33.202.161 – 176.33.202.166
6 | 176.33.202.168 | /29 | 176.33.202.175 | 176.33.202.169 – 176.33.202.174
6 | 176.33.202.176 | /29 | 176.33.202.183 | 176.33.202.177 – 176.33.202.182
4 | 176.33.202.184 |  |  | 
4 |  |  |  | 
10110000 . 00100001 . 1100101 0 . 10111000
184

## Slide 41: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 | /25 | 176.33.202.127 | 176.33.202.1 – 176.33.202.126
15 | 176.33.202.128 | /28 | 176.33.202.143 | 176.33.202.129 – 176.33.202.142
15 | 176.33.202.144 | /28 | 176.33.202.159 | 176.33.202.145 – 176.33.202.158
6 | 176.33.202.160 | /29 | 176.33.202.167 | 176.33.202.161 – 176.33.202.166
6 | 176.33.202.168 | /29 | 176.33.202.175 | 176.33.202.169 – 176.33.202.174
6 | 176.33.202.176 | /29 | 176.33.202.183 | 176.33.202.177 – 176.33.202.182
4 | 176.33.202.184 | /30 |  | 
4 |  | /30 |  | 
10110000 . 00100001 . 1100101 0 . 10111000
184

## Slide 42: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 | /25 | 176.33.202.127 | 176.33.202.1 – 176.33.202.126
15 | 176.33.202.128 | /28 | 176.33.202.143 | 176.33.202.129 – 176.33.202.142
15 | 176.33.202.144 | /28 | 176.33.202.159 | 176.33.202.145 – 176.33.202.158
6 | 176.33.202.160 | /29 | 176.33.202.167 | 176.33.202.161 – 176.33.202.166
6 | 176.33.202.168 | /29 | 176.33.202.175 | 176.33.202.169 – 176.33.202.174
6 | 176.33.202.176 | /29 | 176.33.202.183 | 176.33.202.177 – 176.33.202.182
4 | 176.33.202.184 | /30 |  | 176.33.202.185 – 176.33.202.186
4 |  | /30 |  | 
10110000 . 00100001 . 1100101 0 . 10111000
184

## Slide 43: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 | /25 | 176.33.202.127 | 176.33.202.1 – 176.33.202.126
15 | 176.33.202.128 | /28 | 176.33.202.143 | 176.33.202.129 – 176.33.202.142
15 | 176.33.202.144 | /28 | 176.33.202.159 | 176.33.202.145 – 176.33.202.158
6 | 176.33.202.160 | /29 | 176.33.202.167 | 176.33.202.161 – 176.33.202.166
6 | 176.33.202.168 | /29 | 176.33.202.175 | 176.33.202.169 – 176.33.202.174
6 | 176.33.202.176 | /29 | 176.33.202.183 | 176.33.202.177 – 176.33.202.182
4 | 176.33.202.184 | /30 | 176.33.202.187 | 176.33.202.185 – 176.33.202.186
4 |  | /30 |  | 
10110000 . 00100001 . 1100101 0 . 10111000
184

## Slide 44: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 | /25 | 176.33.202.127 | 176.33.202.1 – 176.33.202.126
15 | 176.33.202.128 | /28 | 176.33.202.143 | 176.33.202.129 – 176.33.202.142
15 | 176.33.202.144 | /28 | 176.33.202.159 | 176.33.202.145 – 176.33.202.158
6 | 176.33.202.160 | /29 | 176.33.202.167 | 176.33.202.161 – 176.33.202.166
6 | 176.33.202.168 | /29 | 176.33.202.175 | 176.33.202.169 – 176.33.202.174
6 | 176.33.202.176 | /29 | 176.33.202.183 | 176.33.202.177 – 176.33.202.182
4 | 176.33.202.184 | /30 | 176.33.202.187 | 176.33.202.185 – 176.33.202.186
4 | 176.33.202.188 | /30 |  | 
10110000 . 00100001 . 1100101 0 . 10111000
184

## Slide 45: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 | /25 | 176.33.202.127 | 176.33.202.1 – 176.33.202.126
15 | 176.33.202.128 | /28 | 176.33.202.143 | 176.33.202.129 – 176.33.202.142
15 | 176.33.202.144 | /28 | 176.33.202.159 | 176.33.202.145 – 176.33.202.158
6 | 176.33.202.160 | /29 | 176.33.202.167 | 176.33.202.161 – 176.33.202.166
6 | 176.33.202.168 | /29 | 176.33.202.175 | 176.33.202.169 – 176.33.202.174
6 | 176.33.202.176 | /29 | 176.33.202.183 | 176.33.202.177 – 176.33.202.182
4 | 176.33.202.184 | /30 | 176.33.202.187 | 176.33.202.185 – 176.33.202.186
4 | 176.33.202.188 | /30 |  | 176.33.202.189 – 176.33.202.190
10110000 . 00100001 . 1100101 0 . 10111000
184

## Slide 46: Example 2
# of IPs | Network ID | Mask | Broadcast IP | Range of usable addresses
102 | 176.33.202.0 | /25 | 176.33.202.127 | 176.33.202.1 – 176.33.202.126
15 | 176.33.202.128 | /28 | 176.33.202.143 | 176.33.202.129 – 176.33.202.142
15 | 176.33.202.144 | /28 | 176.33.202.159 | 176.33.202.145 – 176.33.202.158
6 | 176.33.202.160 | /29 | 176.33.202.167 | 176.33.202.161 – 176.33.202.166
6 | 176.33.202.168 | /29 | 176.33.202.175 | 176.33.202.169 – 176.33.202.174
6 | 176.33.202.176 | /29 | 176.33.202.183 | 176.33.202.177 – 176.33.202.182
4 | 176.33.202.184 | /30 | 176.33.202.187 | 176.33.202.185 – 176.33.202.186
4 | 176.33.202.188 | /30 | 176.33.202.191 | 176.33.202.189 – 176.33.202.190
10110000 . 00100001 . 1100101 0 . 10111000
184